COSC 4372 – Assignment 2
Name: Dan Kalhori
PSID: 2153552
9/29/2024
github link:	https://github.com/DanKalh/4372-hw2-fall2024-DanKalh
I	Problem

Q.1 Physical Properties Maps: Generate and present the A-map, T1-map, and T2-map of your phantom.

Q.2.1 Compute the SI for all four compartments using the various acquisition parameters and complete the table below.

Q.2.2 Report the four generated MRIs (one for each set of the acquisition parameters). Add a legend to each image reporting the used acquisition parameter and the calculated SI for each compartment. (10 pts)

Q.2.3 Plot SI versus TR (10 pts). What is your observation regarding the impact of varying TR? (15 pts)

As TR increases, the Signal Intensity also increases, but can sometimes make them seem uniform if increasing too much.

Q.2.4 Fix TR at 250, and adjust TE to 10, 40, and 80, 150. Calculate the SI only for compartment 2 using these TE values (5 pts). Plot the SI versus TE (2 pts). What is your observation regarding the impact of varying TE? (8 pts)

As TE increases (for Compartment 2) the Signal Intensity decreases fairly quickly. It could help to increase contrast even further alongside TR.
Q.3.1 Compute the SSIM (Structural Similarity Index) between the following pairs of images generated in Q.2.1 (10 pts): • Image 1 and Image 2 • Image 1 and Image 3 • Image 1 and Image 4 What do you observe and why (10 pts)?

II	Method

I utilized the Shepp-Logan phantom, where ellipses are used to represent anatomical structures. Each ellipse has parameters for center position, rotation angle, size, and signal intensity. By modifying these parameters, I generated a series of progressively more complex phantom images, starting with basic structures and adding features like circular tumors and concentric ellipses.

III	Implementation

I used MATLAB to implement a modified_phantom function that takes the matrix size, number of ellipses, center positions, rotation angles, sizes, and signal intensities as input parameters. I created three variations:
1. Phantom One: Basic structure with no overlapping ellipses.
2. Phantom Two: Builds on Phantom One by adding circular structures outside the brain (reference).
3. Phantom Three: Creates a phantom with three concentric circles.
The code progressively adds new features and generates each image.

IV	Results

The phantoms successfully represent very basic anatomical features using ellipses. The first phantom shows a basic non-overlapping structure, the second adds external circular features(for reference as mentioned in class), and the third creates a set of concentric circles although kind of used throughout to for a “head”. These phantoms can be used for testing imaging algorithms.

Modified Phantom:
function phantom_image = dynamic_phantom(N, M, center_positions, rotation_angles, sizes, signal_intensities)
    % modified_phantom: Generate a custom phantom with dynamic number of ellipses.
    % Inputs:
    % N - Phantom matrix size (NxN).
    % M - Number of ellipses.
    % center_positions - Mx2 matrix, where each row is [X, Y] for ellipse center.
    % rotation_angles - Mx1 vector, each element is the rotation angle (in degrees).
    % sizes - Mx2 matrix, where each row is [width, height] of the ellipse.
    % signal_intensities - Mx1 vector, signal intensity of each ellipse.
    %
    % Outputs:
    % phantom_image - The generated phantom image.

    % Initialize the phantom matrix to zeros
    phantom_image = zeros(N);

    % Generate x and y axis grids that span [-1, 1]
    x_axis = ((0:N-1) - (N-1)/2) / ((N-1)/2);
    x_grid = repmat(x_axis, N, 1); % X coordinates
    y_grid = rot90(x_grid); % Y coordinates

    % Loop through each ellipse and add it to the phantom
    for k = 1:M
        % Extract ellipse properties for the current ellipse
        center_x = center_positions(k, 1);
        center_y = center_positions(k, 2);
        rotation_angle = rotation_angles(k);
        semi_axis_a = sizes(k, 1) / 2; % Horizontal semi-axis (width / 2)
        semi_axis_b = sizes(k, 2) / 2; % Vertical semi-axis (height / 2)
        signal_intensity = signal_intensities(k);

        % Convert rotation angle to radians
        rotation_angle_rad = rotation_angle * pi / 180;

        % Shift the x and y grids by the ellipse center position
        x_shifted = x_grid - center_x;
        y_shifted = y_grid - center_y;

        % Rotate the coordinates based on the rotation angle
        x_rotated = x_shifted * cos(rotation_angle_rad) + y_shifted * sin(rotation_angle_rad);
        y_rotated = -x_shifted * sin(rotation_angle_rad) + y_shifted * cos(rotation_angle_rad);

        % Equation of the ellipse (normalized form)
        ellipse_equation = (x_rotated.^2) / (semi_axis_a^2) + (y_rotated.^2) / (semi_axis_b^2);

        % Find pixels inside the ellipse (where equation is <= 1)
        ellipse_mask = ellipse_equation <= 1;

        % Add the ellipse to the phantom with the specified signal intensity
        phantom_image(ellipse_mask) = phantom_image(ellipse_mask) + signal_intensity;
    end
end